## Slide 1: A Hardware-assisted Translation Cache for Dynamic Binary Translation in Embedded Systems
Filipe Salgado, Tiago Gomes, Adriano Tavares, and Jorge Cabral
2018 IEEE 23rd International Conference on Emerging Technologies and Factory Automation (ETFA)

## Slide 2: Outline
Introduction
Hardware-assisted Translation Cache
Evaluation
Conclusion

## Slide 3: Outline
Introduction
Hardware-assisted Translation Cache
Evaluation
Conclusion

## Slide 4: Introduction
This paper base on another paper
Y. Yao, Z. Lu, Q. Shi, and W. Chen, “FPGA based hardware-software co-designed dynamic binary translation system,” 2013 23rd International Conference on Field Programmable Logic and Applications, FPL 2013- Proceedings. IEEE Computer Society., pp. 0–3, 2013.

## Slide 5: Dynamic Binary Translation(DBT)
Dynamic binary translation (DBT) is a technique that was developed for architectural compatibility, i.e., to run machine binary code on architectures different from the one it was compiled for.

## Slide 6: Translation Cache (TCache)
Tcache is a translation buffer where the translated code is stored prior its execution
It requires different features from the source binaries cache.
  Write and Execution Privileges
  Content Management
  Eviction Mechanism

## Slide 7: Outline
Introduction
Hardware-assisted Translation Cache
Evaluation
Conclusion

## Slide 8: Flowchart of the HW/SW co-designed DBT system

## Slide 9: Problem
This approach relies on a heavy software-based backup mechanism to handle missing translations from the hardware management.
The software hash table mechanism should be avoided in the resource-constrained embedded systems, because of the well known latency it originates.

## Slide 10: Solution
The implemented approach avoids the use of the software hash table through an adjustment to the new entry insertion mechanism of LUT.
The new entries are inserted sequentially until the insertion index overflows and starts to overwrite the first entries.

## Slide 11: Problem of the solution
The eventual look-ups of overwritten entries will generate a false miss because the translation is indeed stored at the TCache allocated memory, but its look-up position was given to another TBBs.

## Slide 12: Outline
Introduction
Hardware-assisted Translation Cache
Evaluation
Conclusion

## Slide 13: Experimental Environment
Benchmark: Bristol Energy Efficiency Benchmark Suite (BEEBS)
Source ISA: Intel 8051
Target ISA: Arm Cortex-M3
The tests were repeated for four different TCache sizes: 4 KB, 8 KB, 16 KB and 32 KB.

## Slide 14: TCache size variation

## Slide 15: Software-based TCache mechanisms

## Slide 16: Hardware-assisted TCache vs. Software-based TCache

## Slide 17: Outline
Introduction
Hardware-assisted Translation Cache
Evaluation
Conclusion

## Slide 18: Conclusion
This article addresses the functionality extension of the DBT engine using external hardware support.
The hardware LUT has a reduced and fixed insertion and search time, leading to better performance and scalability